## Slide 1: Carbon crystal -- insulator

## Slide 2: Silicon behaves similarly
14 total electrons
2 in the inner shell
8 in the middle shell
4 in the outer shell

## Slide 3: Boron and Phosphorous

## Slide 4: Doped Silicon

## Slide 5: PN Junction (diode)

## Slide 7: Single Processor Performance
Introduction

## Slide 8: Sample DVFS
Example P-State Table | 
Voltage | Frequency
1.21 V | 2.8 GHz (HFM)
1.18 V | 2.4 GHz
1.05 V | 2.0 GHz
0.96 V | 1.6 GHz
0.93 V | 1.3 GHz
0.86 V | 900 MHz
0.80 V | 600 MHz (LFM)
https://en.wikichip.org/wiki/intel/frequency_behavior

## Slide 9: Sample DVFS
Example P-State Table |  |  |  | 
Voltage | Frequency | Cost | Relative Cost | Time / CPU increase
1.21 V | 2.8 GHz (HFM) | 1.46 | 1.0 | 1.0
1.18 V | 2.4 GHz | 1.39 | 0.95 | 1.16
1.05 V | 2.0 GHz | 1.10 | 0.75 | 1.4
0.96 V | 1.6 GHz | 0.92 | 0.63 | 1.75
0.93 V | 1.3 GHz | 0.86 | 0.59 | 2.15
0.86 V | 900 MHz | 0.74 | 0.51 | 3.11
0.80 V | 600 MHz (LFM) | 0.64 | 0.43 | 4.66
https://en.wikichip.org/wiki/intel/frequency_behavior

## Slide 10: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance

## Slide 11: Single-Cycle vs. Pipelined Performance

## Slide 12: Fallacies and Pitfalls
Microprocessors are a silver bullet
  Performance is now a programmer’s burden
Falling prey to Amdahl’s Law
A single point of failure
Hardware enhancements that increase performance also improve energy efficiency, or are at worst energy neutral
Benchmarks remain valid indefinitely
  Compiler optimizations target benchmarks

## Slide 13: Fallacies and Pitfalls
The rated mean time to failure of disks is 1,200,000 hours or almost 140 years, so disks practically never fail
  MTTF value from manufacturers assume regular replacement
Peak performance tracks observed performance
Fault detection can lower availability
  Not all operations are needed for correct execution